## Slide 1: MPSS – The Software Stack
Ravi Murty, Intel
ravi.murty@intel.com

## Slide 2: Legal Disclaimer
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPETY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL’S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL® PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
Intel may make changes to specifications and product descriptions at any time, without notice.
All products, dates, and figures specified are preliminary based on current expectations, and are subject to change without notice.
Intel, processors, chipsets, and desktop boards may contain design defects or errors known as errata, which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Sandy Bridge and other code names featured are used internally within Intel to identify products that are in development and not yet publicly announced for release. Customers, licensees and other third parties are not authorized by Intel to use code names in advertising, promotion or marketing of any product or services and any such use of Intel's internal code names is at the sole risk of the user
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more information go to http://www.intel.com/performance
Intel, Core, Xeon, VTune, Cilk, Intel and Intel Sponsors of Tomorrow. and Intel Sponsors of Tomorrow. logo, and the Intel logo are trademarks of Intel Corporation in the United States and other countries.
*Other names and brands may be claimed as the property of others.
Copyright ©2011 Intel Corporation.
Hyper-Threading Technology: Requires an Intel® HT Technology enabled system, check with your PC manufacturer. Performance will vary depending on the specific hardware and software used. Not available on all Intel® Core™ processors. For more information including details on which processors support HT Technology, visit http://www.intel.com/info/hyperthreading
Intel® 64 architecture: Requires a system with a 64-bit enabled processor, chipset, BIOS and software. Performance will vary depending on the specific hardware and software you use. Consult your PC manufacturer for more information. For more information, visit http://www.intel.com/info/em64t
Intel® Turbo Boost Technology: Requires a system with Intel® Turbo Boost Technology capability. Consult your PC manufacturer. Performance varies depending on hardware, software and system configuration. For more information, visit http://www.intel.com/technology/turboboost

## Slide 3: Agenda
Section 1: The System SW Stack
  Card OS
  Symmetric Communications Interface (SCIF)
  Code Examples
Section 2: Compiler Runtimes
  Coprocessor Offload Infrastructure (COI)
  Code Examples
Section 3: Coprocessor Communication Link (CCL)
  IB-SCIF
  CCL Direct and Proxy
  MPI Dual-DAPL
Section 4: Heterogeneous Programming with Offload
  Code Examples
iXPTC 2013
Intel® Xeon Phi ™Coprocessor

## Slide 4: Intel® Xeon Phi™ Coprocessor Arch – System SW Perspective
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Large SMP UMA machine – a set of x86 cores to manage
  4 threads and 32KB L1I/D, 512KB L2 per core
  Supports loadable kernel modules – we’ll talk about one today
Standard Linux kernel from kernel.org
  2.6.38 in the most recent release
  Completely Fair Scheduler (CFS), VM subsystem, File I/O
Virtual Ethernet driver– supports NFS mounts from Intel® Xeon Phi™ Coprocessor
New vector register state per thread for Intel® IMCI
  Supports “Device Not Available” for Lazy save/restore
Different ABI – uses vector registers for passing floats
  Still uses the x86_64 ABI for non-float parameter passing (rdi, rsi, rdx ..)

## Slide 5
Card OS

## Slide 6: Card OS
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Bootstrap
  Memory training
  Build MP Table, e820 map, load image in memory (bzImage)
  Jump to 32-bit protected mode entry point in the kernel
It’s just Linux with some minor modifications:
    IPI format, local APIC calibration, no support for compatibility mode (CSTAR)
    No global bit in PTE/PDE entries.
    IOAPIC programmed via MMIO
    Instructions not supported: cmov, in/out, monitor/mwait, fence
    No support for MMX/SSE registers
    Save/restore of vector state via DNA (CR0.TS=1)

## Slide 7: Execution Modes
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
main()
Intel ® Xeon Phi™
Coprocessor
Intel® Xeon
main()
Native
Offload
Card is an SMP machine running Linux
Separate executables run on both MIC and Xeon
  e.g. Standalone MPI applications
No source code modifications most of the time
  Recompile code for Xeon Phi™ Coprocessor
Autonomous Compute Node (ACN)
“main” runs on Xeon
Parts of code are offloaded to MIC
Code that can be
  Multi-threaded, highly parallel
  Vectorizable
  Benefit from large memory BW
Compiler Assisted vs. Automatic
  #pragma offload (…)
foo()
Intel® Xeon
main()
Intel® Xeon Phi™
Coprocessor

## Slide 8: Native is Easy
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Cross compile your application for k1om arch
  Intel C/C++ and Fortran compiler, k1om aware GCC port.
  Binutils for k1om e.g. objdump
  LSB – glibc, libm, librt, libcurses etc.
  Busybox – minimal shell environment
Virtual Ethernet driver allows:
  ssh, scp
  NFS mounts
You still have to spend time parallelizing and vectorizing your application for performance on Intel® Xeon Phi™ Coprocessor

## Slide 9: “Hello World”
iXPTC 2013
Intel® Xeon Phi ™Coprocessor

## Slide 10: Performance Considerations for Native
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Single vs. Multi-threaded applications
  Scalability is important
Scalar vs. Vector code
Explicit cache management
  SW prefetching and evicting
Chart: 
| Scalar & ST | Vector & ST | Scalar & MT | Vector & MT | Scalar BW | MT BW
Xeon | 2.6 | 41.6 | 41.6 | 665.6 | 9.8 | 67
Xeon Phi | 1.09 | 34.88 | 66.49 | 2127.68 | 6.5 | 200
 | Frequency | cores | vector width
Xeon | 2.6 | 16 | 8
Xeon Phi™ Coprocessor | 1.09 | 61 | 16
log scale
Peak flops (Gflop/s)
Intel® Xeon Phi™ Coprocessor has a Fused Multiply Add (FMA) for 2x flops/cycle

## Slide 11: DMA alignment results
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Case2: CU + MA (16, 272)
Case1: CA
Case3: CU + MU (16, 84)
(x, y) – x = source offset, y = destination offset
CA – Cacheline Aligned
CU – Not Cacheline Aligned
MA – Mutually Aligned between source and destination buffers
MU – Mutually Mis-aligned between source and destination buffers
Chart: 
Chart: 
Chart: 
8K – 6.7 GB/s
16 K – 6.8 GB/s
8K – 3.4 GB/s
16 K – 5.9 GB/s
8K – 0.95 GB/s
16 K – 1.6 GB/s
Source: Michael Carroll, MPSS Team

## Slide 12: Coprocessor Offload Infrastructure (COI)
iXPTC 2013
Intel® Xeon Phi ™Coprocessor

## Slide 13
Card OS

## Slide 14: COI Introduction
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
COI provides a set of APIs to simplify development for tools/apps using offload accelerator models
  Simplifies running application on the Intel® Xeon Phi™ Coprocessor
    Loading and launching device code without needing SSH passwords, NFS mounts, etc.
  Simplifies asynchronous execution and data transfer
    Can set up dependencies between asynchronous code execution and data movement
    Device parallelism keeps the host, DMA engines and Phi device busy at the same time
  Simplifies Resource Management
    Automatically manages buffer space by reserving memory and evicting data as needed
  Simplest way to get the best performance
    COI includes features such as pinned buffers and same address buffers which make it easy to offload existing applications

## Slide 15: COI Terminology
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
source
sink
Xeon
Xeon Phi™
Coprocessor
forward
offload
COI allows commands to be sent from a “source” to a “sink”
  Commands are asynchronous function invocations (“run functions”)
  “Source” is where “run functions” are initiated
  “Sink” is where “run functions” are executed
A typical COI application is comprised of a source application and a sink offload binary
The sink binary is a complete executable
  Not just a shared library
  Starts executing from main when it is loaded
COI automatically loads dependent libraries prior to starting the offload binary on the sink
COI has a coi_daemon that spawns sink processes and waits for them to exit

## Slide 16: Host and Device Parallelism with COI
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
This of the instruction execution pipeline - Hennessy and Patterson
Host Compute
DMA to Device
Device Compute
DMA to Host
Host Compute
DMA to Device
Device Compute
DMA to Host
Host Compute
DMA to Device
Device Compute
DMA to Host
Host Compute
DMA to Device
Device Compute
Host Compute
DMA
to Device
Host Compute
Host, device, and DMA all busy at the same time!
(if necessary)

## Slide 17: COI APIs – First glance
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
COI exposes four major abstractions:
  Use the simplest layer or add additional capabilities with more layers as needed
  Each layer intended to interoperate with other available lower layers (e.g. SCIF)
Enumeration: COIEngine, COISysInfo
  Enumerate HW info; cards, APIC, cores, threads, caches, dynamic utilization
Process Management: COIProcess (requires COIEngine)
  Create remote processes; loads code and libraries, start/stop
Execution Flow: COIPipeline (requires COIProcess)
  COIPipelines are the RPC-like mechanism for flow control and remote execution
  Can pass up to 32K of data with local pointers
Data and Dependency Management: COIBuffer, COIEvent (requires COIPipeline)
  COIBuffers are the basic unit of data movement and dependence managment
  COIEvent optionally used to help manage dependences
  COIBuffers and COIEvents are typically used with Run Functions executing on COIPipelines

## Slide 18: API: COIEngine
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
Abstracts the devices in the system
  Host x86_64 device as well as Phi cards
Provides device enumeration capabilities
  Number of devices and handles to devices
Also provides dynamic device information
  Current memory utilization and CPU load
Does not require any other COI APIs
/* Get the number of engines */
uint32_t num_engines = 0;
COIEngineGetCount(COI_ISA_MIC, /* The type of engine. */
&num_engines); /* Outparam for number of engines */
/* of this type. */
/* Get a handle to the first one */
COIENGINE engine;
COIEngineGetHandle(COI_ISA_MIC, /* The type of engine.
0, /* The index of the engine within
* the array of engines of this type
*/
&engine); /* Outparam for the engine handle */

## Slide 19: Coprocessor Communication Link (CCL)
iXPTC 2013
Intel® Xeon Phi ™Coprocessor

## Slide 20
Card OS

## Slide 21: Introduction
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
  OFED is the industry standard code used for messaging on high-end HPC clusters
    Supports Intel MPI and all open source MPIs
    Is in Linux and all the various Linux distributions
  RDMA over SCIF (IB-SCIF) – RDMA within the platform between the host and KNC or multiple KNCs
  Intel ® Xeon Phi ™ Coprocessor Communication Link (CCL) Direct
    Direct access to InfiniBand HCA from Intel® Xeon Phi ™
    Lowest latency data path
  Intel ® Xeon Phi ™ Coprocessor Communication Link (CCL) Proxy
    Pipeline data through host memory to InfiniBand network
    Higher bandwidth data path for some platform configurations
  Intel MPI dual-DAPL support
    Uses best data path, direct path for small messages, and proxy path for large messages for best overall MPI performance

## Slide 22: RDMA over IB-SCIF
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
OFED for Intel® Xeon Phi™ Coprocessor uses the core OFA software modules from the Open Fabrics Alliance
IB-SCIF is a new hardware specific driver and library that plugs into the OFED core mid-layer
  SCIF is the lowest level in the SW stack as we saw earlier
  Provides standard RDMA verbs interfaces within the platform, i.e., between the Intel® Xeon™ and Intel® Xeon Phi ™ Coprocessor cards within the same system.
    IBSCIF 1 byte latency is in the 13us range, (host-KNC), peak BW is in the 6GB/s per sec. range
Xeon Host /Xeon Phi

## Slide 23: Intel® Xeon Phi ™ Coprocessor CCL Direct Software
iXPTC 2013
Intel® Xeon Phi ™Coprocessor
CCL-Direct
  Allows access to an HCA directly from the Xeon Phi™ Coprocessor using standard OFED interfaces using PCI-E peer-to-peer transactions
  Provides the lowest latency data path
  For each hardware HCA, a unique vendor driver has to be developed.
    e.g., mlx4, mthca, Intel® True Scale ™ hca etc
    Currently support for Mellanox HCAs (mlx4) exists and is shipping in MPSS
    Support for Intel® TrueScale™ InfiniBand NICs via PSM is under development, expected release in early 2013
Implementation Limitations
  Intel® Xeon Phi™ Coprocessor CCL Direct only supports user space clients, e.g. MPI
  Peak bandwidth is limited on some platforms and configurations
  CCL-Direct 1 byte latency is in the 2.5us range for Host-KNC, and 3.5-4us range for KNC-KNC across an InfiniBand HCA, peak BW varies depending on the Xeon platform (see later)

## Slide 25: Backup Material

## Slide 26: SCIF Backup Material

## Slide 27
Connection Process
SCIF connection process is very socket-like
Open an endpoint, ep, and bind it to some port, pn
Mark the port as a listening port
Wait for a connection request, then Accept the connection request and return a new endpoint, nepd
The peer processes can communicate through the completed connection
Open an endpoint, ep, and bind it to some port, pn
Request a connection to port pn on node j Connection is complete on return
The peer processes can communicate through the completed connection

## Slide 28
Launching Remote Processes
Connection requires one process to listen and one to request a connection
How do you get a process on a node that will accept your connection request?
Some ports are “well known” and reserved for specific clients
  COI, MYO, OFED, RAS, PM, NetDev
  Each client typically has a daemon (launched with uOS at R3 or R0)
Other apps can use services such as COI, micnativeloadex, or ssh (over virtual Ethernet) to launch a process on a node

## Slide 29
Kernel mode APIs
int scif_pin_pages(void *addr, size_t len, int prot_flags, int map_flags, scif_pinned_pages_t *pinned_pages);
int scif_unpin_pages(scif_pinned_pages_t pinned_pages);
off_t scif_register_pinned_pages( scif_epd_t epd, scif_pinned_pages_t pinned_pages, off_t offset, int map_flags);
int scif_get_pages(scif_epd_t epd, off_t offset, size_t len, struct scif_range **pages);
int scif_put_pages(struct scif_range *pages);
int scif_event_register(scif_callback_t handler);
int scif_event_unregister(scif_callback_t handler);
int scif_pci_info(uint16_t node, struct scif_pci_info *dev);

## Slide 30: SCIF APIs at a glance
Endpoint connection:
  connection establishment between processes
  scif_open(), scif_bind(), scif_listen(), scif_accept(), scif_connect(), scif_close()
Messaging:
  send/receive messages between connected endpoints
  scif_send(), scif_recv()
  A message is an arbitrary sequence of bytes
  These APIs are intended to be used for short data transfers e.g. commands
Registration:
  Exposes local physical memory for remote access via a local Registered Address Space
  scif_register(), scif_unregister()
Mapping:
  scif_mmap(), scif_munmap()
  Maps remote physical pages into local virtual address space of process

## Slide 31: SCIF APIs at a glance (2)
Remote Memory Access (RMA):
  Perform DMA or programmed I/O transfers
  scif_readfrom(), scif_writeto(), scif_vreadfrom(), scif_vwriteto()
  Supports the notion of “one sided communication”
    Push or pull data
  Supports DMA (for large) or CPU (for small transfers) based transfers
Synchronization:
  Enables synchronization with RMA completion, now vs. later
  Must comprehend RMAs completing out of order – multiple DMA channels
  Scif_fence(), scif_fence_mark(), scif_fence_wait(), scif_fence_signal()
Utility:
  scif_get_nodeIDs(), scif_poll(), scif_get_fd()
Requires HW support to make all of this work (and work well)
  PCIe accesses
  SMPT
  Aperture mapped from the host
  Interrupts in both directions (ICR and System interrupt registers)

## Slide 32: 声明：
所有的版权属于原有公司，文件均来自公开渠道
此文件仅供学习使用，任何人不得进行以此为商业目的的行为
如有疑问，请立即删除
https://www.chuanke.com
https://study.163.com
学习世界五百强和咨询公司PPT课程请访问如下网站搜索：“司马懿”
https://www.zhiu.com
百度传课：司马懿PPT学校
网易学堂：司马懿PPT学校
知乎： 司马懿PPT学校